## Slide 1
Synchronous Buck Converter with Zero-Voltage Resonant-Transition Switching
Simple Soft Switching
Additional passive and active components or a complicated loop control is not required
High conduction current due to high current ripple
Synchronous buck converter
Required condition for soft-switching:
Output load resitance
The ratio between the peak-to-peak inductor current ripple and the average inductor current
K is proportional to input voltage
K is inv. prop. to maximum output current

## Slide 2
Spike on the switching current is removed
Unfortunately, the switching losses are still non-zero

## Slide 3
DC
AC
Average Transition Time
Loss Calculation
GS66508T
650V / 30A
Top Cooling
Rds-on (150˚C) -> 129 mΩ
Coss -> 88 pF
Transistor Parameters
Inductor Current

## Slide 4
Loss Analysis
Vin = 540V
Vout = 400V
Iout = 20A
Pout = 8 kW
K = 4
Rise Time = 10 nsec
4 Parallel Transistor
3 Parallel Transistor

## Slide 5
Loss Analysis
Vin = 540V
Vout = 400V
Iout = 10A
Pout = 4 kW
K = 4
Rise Time = 10 nsec
4 Parallel Transistor
2 Parallel Transistor

## Slide 6
Loss Analysis
Vin = 220V
Vout = 150V
Iout = 20A
Pout = 3 kW
K = 4
Rise Time = 10 nsec
4 Parallel Transistor
3 Parallel Transistor

## Slide 7
Loss Analysis
Vin = 220V
Vout = 150V
Iout = 10A
Pout = 1.5 kW
K = 4
Rise Time = 10 nsec
4 Parallel Transistor
3 Parallel Transistor

## Slide 8
Simulation Study

## Slide 9
Simulation Study
K = 0.25 -> Hard-switching Vin = 540V
Vout = 400V, Pout = 8 kW
fsw = 100 kHz, Tj = 25˚C
Top Switch
Power Loss 7.1296 W
Bottom Switch
Power Loss 0.432 W
Total Transistor Loss = 30.2464 W
4 App Ripple

## Slide 10
Simulation Study
K = 4 -> Soft-switching Vin = 540V
Vout = 400V, Pout = 8 kW
fsw = 100 kHz, Tj = 25˚C
Top Switch
Power Loss 2.2542 W
Bottom Switch
Power Loss 0.979 W
Total Transistor Loss = 12.9328 W
80 App Ripple
%57

## Slide 11
Simulation Study
K = 4 -> Soft-switching Vin = 540V
Vout = 400V, Pout = 8 kW
fsw = 100 kHz, Tj = 125˚C
Top Switch
Power Loss 5.3075 W
Bottom Switch
Power Loss 2.1791 W
Total Transistor Loss = 29.9464 W
80 App Ripple
%37

## Slide 12
Simulation Study
Seperated Switching Nodes for Interleaving

## Slide 13
Simulation Study
Advantages of Interleaved Half-Bridges for ZVRT Switching Buck Converter Application
The average output current is shared between two inductors which reduces average inductor current
Having less average inductor current requires less ripple current (K *Iavg)
Applying 180˚ phase shift between two half-bridges reduces stress over output capacitor significantly
What we get from interleaving

## Slide 14
Simulation Study
K = 4 -> Soft-switching Vin = 540V
Vout = 400V, Pout = 8 kW
fsw = 100 kHz, Tj = 125˚C
With Interleaving
Top Switch
Power Loss 5.2144 W
Bottom Switch
Power Loss 2.0775 W
Total Transistor Loss = 29.1676 W
26 App Ripple @ 200 kHz
%15

## Slide 15
Simulation Study – Filter Design
Capacitor Current
7.5 Arms @200kHz
ESMM451VSN331MQ50S
Digikey Link – 4.98$
Capacitance: 330 μF
Rated Voltage: 450V
Rated Current: 3A @ 100kHz
ESR: 1.005ohm @120Hz
Three of this capacitor are required!

## Slide 16
Simulation Study – Filter Design
Capacitor Current
7.5 Arms @200kHz
C4AQCBW5200A3FJ
Digikey Link – 4.82$
Capacitance: 20 μF
Rated Voltage: 650V
Rated Current: 11A @ 10kHz
ESR: 5.3 mOhm @10kHz
Only one of this capacitor is required!

## Slide 17
Simulation Study – Filter Design
Inductor Current
26 μH
15 Arms @100kHz
10 Adc
30A, -10A peak points
1140-330K-RC
Digikey Link – 9.56$
Inductance: 33 μH @1KHz
Rated Current: 15.8 A
Sat. Current: 36.5 A
DCR: 11 mOhm
Two of this inductor are required!
7443783533330
Digikey Link – 14.02$
Inductance: 33 μH @100KHz
Rated Current: 22 A
Sat. Current: 39.2 A
DCR: 9.9 mOhm
Option #1
Option #2
Self-Resonance?
Can cause hard-switching

## Slide 18
Simulation Study – Filter Design
L1 Ratings
13.9 Arms @100kHz
9.2 Adc
27.1A, -8.8A peak points
Inductance Tolerances (+/-10%)
L2 Ratings
16.75 Arms @100kHz
10.8 Adc
32.7A, -10.6A peak points
C Ratings
7.9 Arms @200kHz
L Ratings
15 Arms @100kHz
10 Adc
30A, -10A peak points
C Ratings
7.5 Arms @200kHz
Balanced Ind.
Unbalanced Ind.
Unbalanced conditions
don’t seem that harmful!

## Slide 19
Simulation Study with Selected Filters
 | Results before filter selections | Results after filter selections
I(C) | 26 App @200 kHz | 20 App @200 kHz
I(L) | 15 Arms | 13.5 Arms
Ipeak(L) | 30 A, -10 A | 25.6 A, -5.6 A
Ploss(top switch) | 5.2144 W | 4.805 W
Ploss(bot switch) | 2.0775 W | 1.9416 W
Ploss(total) | 29.17 W | 27 W
Vout,pp | 0.8 V | 0.4 V
The main change is filter inductance. It is changed from 26 μH to 33 μH!

## Slide 20
Simulation Study with Different Switching Frequencies
 | Results for 100 kHz | Results for 300 kHz
I(C) | 26 App @200 kHz | 26 App @600 kHz
I(L) | 15 Arms @100 kHz | 15 Arms @300 kHz
Ipeak(L) | 30 A, -10 A | 30 A, -10 A
Ploss(top switch) | 4.805 W | 6.05 W
Ploss(bot switch) | 1.9416 W | 3.04 W
Ploss(total) | 27 W | 36.4 W
Vout,pp | 0.4 V | 0.8 V
The main gain is volume.
Inductance and capacitance requirements are now one-third!
What about the heatsink?

## Slide 21
Simulation Study with Different Negative Gate Drive Levels
Vgs (0V)
Vgs (-3V)
5.12 W
4.805 W
Top Transistor

## Slide 22
Simulation Study with Different Negative Gate Drive Levels
Vgs (0V)
Vgs (-3V)
1.85 W
1.94 W
Bot Transistor

## Slide 23
Simulation Study with Parasitics
Soft-switching
Hard-switching
Turn-off Event
There is 1 nH CSI difference for top switch

## Slide 24
Simulation Study with Parasitics
Soft-switching
Hard-switching
Turn-on Event
There is 1 nH CSI difference for top switch