## Slide 1
Parallel Bridge DPT Results

## Slide 2
Parallel Bridge DPT Results
Control switch waveforms
Parallel switches act together

## Slide 3
Single Bridge DPT Results
Control switch waveforms
Parallel switches act together

## Slide 4
Parallel Bridge DPT Results
Synch switch waveforms

## Slide 5
Single Bridge DPT Results
Synch switch waveforms
Parallel switches act together

## Slide 6
Thermal Tests

## Slide 7
Thermal Tests
Controlled loss is applied to transistors
Applied loss is significantly dependent on the junction temperature

## Slide 8
Thermal Tests
Controlled loss is applied to transistors
Applied loss is significantly dependent on the junction temperature

## Slide 9
Thermal Tests
0.5 C/W
18 C
Measured
Tcase-top -> 100 ˚C
Tcase-bot -> 90 ˚C
Power Loss -> 7.09A2*0.05Ω = 2.5 W (Wrong)
Here having different temperatures between top and bottom temperatures is quite intersting.
Wider copper area for source pin of bottom transistor
Smaller copper area for source pin of top transistor

## Slide 10
Thermal Tests
0.5 C/W
3.5 C/W
15.87 C/W
18 C
Measured
Theatsink -> 69.8 C
Vgan = 435 mV
Igan = 7.5 A
Ploss = 3.26 W
Thermal resistance of HS 15.87 C/W heatsink resist.
Estimated J. Temp = 83 C
7.5 A source current

## Slide 11
Thermal Tests
0.5 C/W
3.5 C/W
15.87 C/W
18 C
Measured
Theatsink -> 64.5 C
Vgan = 389 mV
Igan = 7 A
Ploss = 2.723 W
7 A source current
Analytical
Theatsink(calculated) = 61.2 C
The environment was hotter it might be 1 or 2 celcius higher

## Slide 12
Thermal Tests
0.5 C/W
3.5 C/W
15.87 C/W
18 C
Measured
Theatsink -> 53.7 C
Vgan = 305 mV
Igan = 6 A
Ploss = 1.83 W
6 A source current
Analytical
Theatsink(calculated) = 47 C

## Slide 13
Thermal Tests
0.5 C/W
3.5 C/W
15.87 C/W
18 C
What is estimated?
If we use the better TIM pad, Rtim will be 2.5 K/W
For 6 mm HS with Fan
  Rhs = 4.6 K/W
  Maximum loss is 12.8 W for 130C of junction
For 10 mm HS with Fan
  Rhs = 3.6 K/W
  Maximum loss is 16.7 W for 130C of junction
For 13 mm HS with Fan
  Rhs = 2.9 K/W
  Maximum loss is 18.6 W for 130C of junction
Fan is a must!
Better TIM
is a must!
16.7 W loss is estimated per half-bridge board under full load