## Slide 1
Synchronous Buck Converter with Zero-Voltage Resonant-Transition Switching
Simple Soft Switching
Additional passive and active components or a complicated loop control is not required
High conduction current due to high current ripple
Synchronous buck converter
Required condition for soft-switching:
Output load resitance
The ratio between the peak-to-peak inductor current ripple and the average inductor current
K is proportional to input voltage
K is inv. prop. to maximum output current

## Slide 2
Spike on the switching current is removed
Unfortunately, the switching losses are still non-zero

## Slide 3
DC
AC
Average Transition Time
Loss Calculation
GS66508T
650V / 30A
Top Cooling
Rds-on (150˚C) -> 129 mΩ
Coss -> 88 pF
Transistor Parameters
Inductor Current

## Slide 4
Loss Analysis
Vin = 540V
Vout = 400V
Iout = 20A
Pout = 8 kW
K = 4
Rise Time = 10 nsec
4 Parallel Transistor
3 Parallel Transistor

## Slide 5
Loss Analysis
Vin = 540V
Vout = 400V
Iout = 10A
Pout = 4 kW
K = 4
Rise Time = 10 nsec
4 Parallel Transistor
2 Parallel Transistor

## Slide 6
Loss Analysis
Vin = 220V
Vout = 150V
Iout = 20A
Pout = 3 kW
K = 4
Rise Time = 10 nsec
4 Parallel Transistor
3 Parallel Transistor

## Slide 7
Loss Analysis
Vin = 220V
Vout = 150V
Iout = 10A
Pout = 1.5 kW
K = 4
Rise Time = 10 nsec
4 Parallel Transistor
3 Parallel Transistor

## Slide 8
Simulation Study

## Slide 9
Simulation Study
K = 0.25 -> No synch. switch Vin = 540V
Vout = 400V, Pout = 8 kW
fsw = 100 kHz, Tj = 25˚C
Top Switch
Power Loss 7.1296 W
Bottom Switch
Power Loss 0.432 W
Total Transistor Loss = 30.2464 W
4 App Ripple

## Slide 10
Simulation Study
K = 4 -> Synch. switch Vin = 540V
Vout = 400V, Pout = 8 kW
fsw = 100 kHz, Tj = 25˚C
Top Switch
Power Loss 2.2542 W
Bottom Switch
Power Loss 0.979 W
Total Transistor Loss = 12.9328 W
80 App Ripple
%57

## Slide 11
Simulation Study
K = 4 -> Synch. switch Vin = 540V
Vout = 400V, Pout = 8 kW
fsw = 100 kHz, Tj = 125˚C
Top Switch
Power Loss 5.3075 W
Bottom Switch
Power Loss 2.1791 W
Total Transistor Loss = 29.9464 W
80 App Ripple
%37

## Slide 12
Simulation Study
Seperated Switching Nodes for Interleaving

## Slide 13
Simulation Study
Advantages of Interleaved Half-Bridges for ZVRT Switching Buck Converter Application
The average output current is shared between two inductors which reduces average inductor current
Having less average inductor current requires less ripple current (K *Iavg)
Applying 180˚ phase shift between two half-bridges reduces stress over output capacitor significantly
What we get from interleaving

## Slide 14
Simulation Study
K = 4 -> Synch. switch Vin = 540V
Vout = 400V, Pout = 8 kW
fsw = 100 kHz, Tj = 125˚C
With Interleaving
Top Switch
Power Loss 5.2144 W
Bottom Switch
Power Loss 2.0775 W
Total Transistor Loss = 29.1676 W
26 App Ripple @ 200 kHz
%15