## Slide 1
FEA Solutions

## Slide 2
FEA Solutions
Comsol
Simplified PCB model is must
Manual meshing
Maxwell 3D
Complex PCB model is fine as long as we are okay with waiting
Automatic meshing is fine

## Slide 3
FEA Solutions

## Slide 4
FEA Solutions
Minimum Inductance Paths

## Slide 5
FEA Solutions
 | Frequency | Inductance | Resistance
Maxwell 3D | 200 MHz | 74.7 nH | 130 mohm
Q3D | 200 MHz | 0.84 nH | 11 mohm
The power loop inductance cannot be 75 nH because DPT under 400V / 40A would result in over-voltage breakdown for sure
This output should be evaluated based on these facts
All capacitors are seperately excited and they are combined in single winding; therefore, all capacitors are connected in series.
Total flux linkage should be divided to total current not a single coil excitation.
We have 6 capacitors
6 turns, for actual inductance divide it by 36 (N2)
Total current excitation is 6 times of the current used by Maxwell
But is it correct?

## Slide 6
FEA Solutions
Each capacitor excitation are seperated into single windings which results in 0.5 nH – 1.8 nH self inductances for each capacitor. Equivalent inductance is the parallel combinations of those inductances: 0.19 nH
But mutual couplings?
0.01 nH < M < 0.5 nH
These two capacitor blocks can be considered as single
Winding #1
Winding #2
 | Winding #1 | Winding #2
Winding #1 | 1 nH | -0.21 nH
Winding #2 | -0.21 nH | 1.5 nH
If we consider these two source in parallel and ignore the mutual coupling, power loop layout inductance is equal to 0.6 nH @200MHz

## Slide 7
This drop on reference level causes false signals

## Slide 8
Capacitive loading is important against sudden changes in circuitry. Two 1 uF ceramic capacitors connected in parallel with resistors
How to solve this problem?

## Slide 10
SCP mechanism is false triggered under this DPT conditions