## Slide 1
Capacitor Selection
SMD component – 0.22uF
(LDEPH3220KA5N00)
(x2)
(x1)
TH component – 0.68uF
(BFC238320684)
+
= 6 Capacitors: 3 Inp + 3 Out

## Slide 2
Capacitor Selection – Bypass Capacitor
IMMD Bypass Capacitors
C3216X7T2W104K160AE – 1206 Package
Capacitance: 100 nF
ESL: 0.75 nH
ESR: 17.5 mohm
Voltage: 450 Vdc
Buck Conv. Bypass Capacitors
C4532X7T2J224M200KC – 1812 Package
Capacitance: 220 nF
ESL: 0.7 nH
ESR: 13.4 mohm
Voltage: 630 Vdc
Effective Capacitance
35 nF
Effective Capacitance
66 nF
Low number of this capacitor can be used

## Slide 3
Heat Sink Selection – Daughter Board Example
Important Disadvantage for Bottom Cooled Transistors
Thermal pad of 516T is 2.3 times of 508T’s thermal pad
TIM is the bottleneck

## Slide 4
Heat Sink Selection – Thermal Resistance Calculation
Assumptions:
Losses are calculated as 4.6 W and 3.8 W for top and bottom transistors. These losses are assumed as 6 W.
Ambient temperature is assumed as 40 ˚C.
Operation temperature is set as 120 ˚C.
Junction-to-case thermal resistance is taken from datasheet and its value is 0.45 ˚C/W.
TIM is selected as A17682-008 and its thermal resistance is calculated as 3.56 K/W. (A better option is A10092-01 and its thermal resistance is 2.28 K/W)
OR
for seperate bridges

## Slide 5
Heat Sink Selection – Option #1
240.13 LFM - 1.22 m/s
Link
Air flow (CFM) is proportional to thickness of fan and its power

## Slide 6
Heat Sink Selection – Option #2
@ 2.75 CFM & 197 LFM
Link - NonStock

## Slide 7
Heat Sink Selection – Option #3
Link
L x W x H – 30.25 x 30.25 x 14.5 - 2.1 C/W @ 200LFM, 1 m/s, 2 CFM

## Slide 8
Heat Sink Selection – Option #4
Link
L x W x H – 30 x 30 x 12.7 - 2.7 C/W @ 200LFM, 1 m/s, 2 CFM
L x W x H – 40 x 40 x 9.5 – 2.5 C/W @ 200LFM, 1 m/s, 3.44 CFM

## Slide 9
Heat Sink Selection – Option #5
Link
L x W x H – 40 x 40 x 24.5 – 2.4 C/W @ 200LFM, 1 m/s, 3.44 CFM

## Slide 10
Heat Sink Selection – Option #6
Link
L x W x H –37.5 x 37.5 x 33 – 2.4 C/W @ 100LFM, 1 m/s, 1.51 CFM