## Slide 1
Noise
@300V
Yellow 5V
Blue LoadCurrent
Lets change the isolated converters
There is a drop on 5V

## Slide 2
Noise
@220V
Yellow 5V
Blue LoadCurrent
Lets connect a capacitor (2.2nF) between SGND and PGND
Hmm, 5V does not drop but SC is triggered.

## Slide 3
Noise
@220V
Yellow Vref
Blue LoadCurrent
Why does SC get triggered if 5V is not distorted? Lets measure Vref
Whenever we touch to measure, it works. If we don’t touch, SC gets triggered.

## Slide 4
Noise
I think we connected Ciso wrong. We should connect it between terminals.

## Slide 5
Noise
@350V
Yellow 5V
Blue LoadCurrent
Lets change the capacitor connection and try
5V drops again, capacitor did not change anything 

## Slide 6
Noise
Why don’t we use the common mode filter. Lets put in series with 5V supply of half-bridge board.
With this configuration it we started to observe problem at 250V. Might it be because we have a longer path?

## Slide 7
Noise
Lets put some capacitor on half-bridge board for 5V bus and see if it helps
We managed to increase voltage up to 350V again with extra 100uF, 3x10uF . 5V drops again down to 4V. Then

## Slide 8
Noise
If it is a differential noise then why don’t we supply isolated converters with anouther source?

## Slide 9
Noise
@350V
Yellow 5V
Blue LoadCurrent
If it is a differential noise then why don’t we supply isolated converters with anouther source?
5V still drops

## Slide 10
Noise
@350V
Yellow Vgsbot
Top Blue with filter
Bot Blue without filter
Lets measure the common mode current for driver converters supply
It seems filter helps, but the problem continues

## Slide 11
Noise
@350V
Yellow Vgsbot
Blue Diff Curr
Lets measure the current of 5V which supplies components other than GD converter
Differential current

## Slide 12
Noise
@350V
Yellow Vgsbot
Blue CM Curr
Lets measure the current of 5V which supplies components other than GD converter
Why is it that similar to differential current

## Slide 13
Noise
@400V
Yellow 5V
Blue Load Curr
Lets see what happens at 400V
It gets completely distorted

## Slide 14
Noise
What about the current of GD converter supply?
Differential current while, common mod filter is connected only to high side supply
@350V
Yellow Vgsbot
Top Blue High Side Supply
Bot Blue Low Side Supply

## Slide 15
Noise

## Slide 16
Noise
Why is 5V still affected by switching where it does not supply anything regardin switching?